# L-16A CPU
Panafacom has introduced the L-16A in April 1975 in the form of a microcomputer based on its experience with minicomputers. In some cases, it may be called PFL-16A with the initial letter of Panafacom. 1 A simple 33 instruction set consisting of Word, a powerful addressing function as in those days including indirect addressing etc., I / O performed via I / O channel, even a CPU issuing a bus right request and permitting use There is a smell of mini-computers, such as mini-computer-like buses that can not use the bus until it comes out or controls with the SEND-ACK signal.
LKit-16, which was released as an evaluation kit for L-16A, was popular because a rare 16-bit CPU was used at that time.
So, this is the CPU, MN 1610. I will post two types of package differences. The MN1610 operates with a 2 MHz two-phase clock, but the 4 MHz version is later manufactured as the MN1610A. I also have this, but photos are omitted.

Below is a package similar to MN1613, which seems to be a late version.
I think that manufacturing is Matsushita from something, model number and mark.
### Architectural overview
It uses 16-bit instructions and data, and has a memory address of 16 bits, but it has the same 40 pins as mainstream 8-bit microprocessors. The address and data signal lines are shared using the same terminals in time division. Memory addresses are assigned in units of words, and there is no way to perform read / write operations in units of bytes as hardware (if using byte-based DMA, control lines can be added from the DMAC to the bus and read / write can be performed in units of bytes) However, the CPU itself can only transfer data in units of words. In order to perform byte-wise data manipulation, it is necessary to combine multiple instructions and program them to extract upper byte or lower byte from word data and vice versa.
The power supply requires +12 V, +5 V, and a slightly odd power supply voltage of -3 V.
There are five general-purpose registers, R0 to R4, as well as stack pointers and status registers. All including the instruction counter are 16 bits wide.
Register name	role
R0	General purpose register
R1	General purpose register
R2	General purpose register
R3 or X0	General purpose register and index register
R4 or X1	General purpose register and index register
SP	Stack pointer
STR	Status register
I c	Instruction counter

General-purpose registers R3 and R4 can also be used as index registers.
It is likely to be beautiful if it is treated as a general-purpose register as R7 up to IC, but it is treated as a special register because it conflicts with the patent of DEC. However, if you read the bit pattern of the L-16A branch instruction, it has a structure that can be interpreted as a load instruction to R7.
The bit assignments for STR are as follows:
E 0 OVF 0 0 M0 M1 M2 Pk Pk Pk Pk Pk Pk Pk Pk
Bit E (MSB) E is an extension register, which is used to perform 16-bit or more operations with addition and subtraction and shift instructions. Also, the OVF in bit 2 is an overflow flag, and changes with overflow detection of the addition and subtraction instruction, and does not change with other instructions. As will be described later, since the L-16A's condition judgment is implemented as part of the operation instruction immediately after the operation, there are no bits corresponding to other flags. If only E and OVF could be used later separately from the skip condition judgment, it would have been adopted because the program is easier to write. Please be assured that the program can detect if the result is negative or 0 properly. M0, M1 and M2 are interrupt masks, 0 means interrupt disabled, 1 means interrupt enabled. As you can see from this, the L-16A interrupt has 3 levels. By the way, the level 0 interrupt equivalent to M0 has the highest priority, and M2 is the lowest level 2 interrupt. There is no maskable interrupt. Level 0 interrupts are generally used for bus blockage detection, memory parity errors, power supply abnormality detection, etc. and correspond to virtually non-maskable interrupts. Level 1 and Level 2 are used for general I / O and timer interrupts. The 8 bits from bit 8 to bit 15 (LSB) of the STR are called program keys and can be used by the programmer for any purpose. Usually, it will be used as some kind of flag.
There are eight types of addressing instructions. 0 page direct, relative direct, index modification to X0 with 8-bit constant, same as index modification to X1 4 types of direct addressing, 0 page indirect, relative indirect, X0 by value obtained by page 0 reference There are a total of eight types of indirect addressing system, four types of index addressing, as well as index qualification to X1. Since the information given to the address constant in the instruction has only 8 bits, for example, in relative addressing, only addresses in the range of -128 to +127 can be specified to the contents of the program counter. In order to access a location that is neither a range of 0 pages nor relative addressing, it is common to define an address constant near the code being executed and to refer to it by relative indirect addressing there. In addition, if it is modified in the range of 8-bit constant by index modification, direct system index modification can be used, but when using 16-bit constant, the constant is stored somewhere on page 0 and indirect system index modification Will be used.
You can use these addressing only for memory reference instructions such as loads, stores, and branches. Normal operation instructions are based on register-to-register operation.
You can specify skip conditions for operation instructions. This is a function that skips the next instruction according to the state of the flag after operation. For example, if the operation result is 0, it will be specified as skip. There are no conditional branch instructions in L-16A, and only one type of unconditional branch instruction, so by placing an unconditional branch instruction in the place where it may be skipped by this skip condition, a normal conditional branch instruction To achieve the same.
The basic instruction of L-16A is as simple as 33 types, all one word instruction. The following shows all instructions.
Meaning assembly language notation
Load L R, EA
Store ST R, EA
Branch B R, EA
Branch and Link BAL R, EA
Increment Memory and
Skip if Result is Zero IMS R, EA
Decrement Memory and
Skip if Result is Zero DMS R, EA
Add A Rd, Rs, Skip
Subtract S Rd, Rs, Skip
Compare C Rd, Rs, Skip
Compare Byte CB Rd, Rs, Skip
Move MV Rd, Rs, Skip
Move Byte MVB Rd, Rs, Skip
Byte Swap BSWP Rd, Rs, Skip
Digit Swap DSWP Rd, Rs, Skip
Load Adjust Part LAD Rd, Rs, Skip
And AND Rd, Rs, Skip
Or OR Rd, Rs, Skip
Exclusive or EOR Rd, Rs, Skip
Operate on E and
Shift Left 1 bit SLR, EM, Skip
Operate on E and
Shift Right 1 bit SR R, EM, Skip
Set Bit SBIT R, I4, Skip
Reset Bit RBIT R, I4, Skip
Test Bit TBIT R, I4, Skip
Add Immediate AIR, I4, Skip
Subtract Immediate SIR, I4, Skip
Load Program Status Word LPSW I2
Halt H
Push the Stack PUSH R
Pop the Stack POP R
Return RET
Read RDR, I8
Write WT R, I8
Move Immediate MVI R, I8
Six instructions from the L instruction to the DMS instruction are instructions for memory manipulation, and the EA indicates the addressing mode and modified constants. R specifies the target register. For memory manipulation instructions, R can specify R0 to R4 (X0 and X1 can be written) and SP. For other instructions R, Rd, and Rs, you can also specify STR. The 12 instructions from the next A instruction to the EOR instruction are binary operation instructions, and after the operation between register registers is performed, the skip condition is judged and the skip operation is performed accordingly. SL and SR are shift instructions, and after performing operations {do nothing, reset, set, invert} specified in EM in 1-bit E register (extension register), E register and specified register Rotate the connected register. Arithmetic shift and rotation can be performed by specifying EM. The SBIT, RBIT, and TBIT instructions are bit operations and perform skip determination operations after manipulating the specified bits. The AI ​​and SI instructions perform skip determination operation after adding or subtracting any value from 0 to 15 to the specified register. LPSW is an interrupt return instruction, which specifies a value from 0 to 2 depending on the interrupt level. From H to RET are literally instructions. RD and WT are operations to the I / O port, and the I / O port address is represented by a constant value of 8 bits. The MVI instruction loads a constant into the low byte of a register.
### Instruction details
#### Memory operation
Let's look at the details of the memory operation instruction.
Memory manipulation instructions include L, ST, B, BAL, IMS, and DMS. These bit patterns are
1 XM M MR R R DDD D DDDD
It is in the form of Bit 0 (MSB) is always 1 and bit 1 can be 0 or 1 depending on the instruction. MMM represents the addressing mode with 3 bits and has the following meaning.
MMM	EA	meaning
0 0 0 0	D	Zero page direct
0 0 1	(IC) + d	Relative direct
0 1 0	[D]	Zero page indirect
0 1 1	[(IC) + d]	Relative indirect
1 0 0	(X0) + D	Constant index
1 0 1	(X1) + D	Constant index
1 1 0	(X0) + [D]	0 page indirect index
1 1 1	(X1) + [D]	0 page indirect index

Here, D is an 8-bit unsigned constant, and d is an 8-bit signed constant.
RRR is a register specification, and it is as follows, but you can not specify STR in the L and ST instructions. In addition, B, BAL, IMS, and DMS do not specify registers, but have bit patterns that identify instructions.
RRR	Register name
0 0 0 0	R0
0 0 1	R1
0 1 0	R2
0 1 1	R3 or X0
1 0 0	R4 or X1
1 0 1	SP
1 1 0	STR
1 1 1	Without using

DDDDDDDD from bit 8 to bit 15 represents an 8-bit constant and is interpreted as signed only for relative addressing.
Here is a description of each instruction.
L instruction and ST instruction
The bit pattern of the L instruction is
1 1 M M MR R R DDD D DDDD
It is in the form of
Similarly, the bit pattern of the ST instruction is
1 0 M M MR R R DDD D DDDD
It is in the form of
MMM and RRR are as above, and you can load and store values ​​to non-STR registers. Although it may seem inconvenient at first glance that STR can not be saved, PUSH / POP is possible, and since it is automatically saved and restored at the time of an interrupt, there is no particular problem. If you really want to store the STR at a specific address, it will be transferred to another register like MVR0, STR and then the contents of that register will be stored.
B instruction
The bit pattern of the B instruction is
1 1 M M M 1 1 1 DDD D DDDD
It is in the form of Jump to the specified address. Because relative addressing is possible, it is possible to branch easily within the range of 8 bits (-128 to +127). However, to jump to a range beyond that, store the address constant in the nearby memory and use relative indirect addressing there. If the variable-length instruction could be designed to handle a 16-bit constant directly by addressing, all instructions have a fixed length of 16 bits, so it looks like this.
BAL command
The bit pattern of the BAL instruction is
1 0 M M M 1 1 1 DDD D DDDD
It is in the form of
The name "branch and link" is called a minicomputer. Although it is a subroutine call instruction, it is possible to leave Link on the stack and move back to the location where it was called by the RET instruction.
IMS and DMS instructions
The bit pattern of the IMS instruction is
1 1 M M M 1 1 0 DDD D DDDD
It is in the form of
The bit pattern of the DMS instruction is
1 0 M M M 1 1 0 DDD D DDDD
It is in the form of
The register specification for the L and ST instructions is STR. Well, that's why I could not specify STR only for L and ST instructions. This is an instruction that uses a specific memory address as a loop counter. The IMS instruction increments the contents of the specified memory and if the result is 0, it skips the next instruction. DMS instructions differ from IMS in that they decrement the specified memory contents. If a B instruction is specified as the instruction to be skipped, the code will loop according to the value stored in the memory in advance.
#### Binary operation instruction
There are 12 types of binary operation instructions. All register-to-register operation. The generalized instruction bit pattern is
0 1 X X X Rd Rd Rd SSS S X Rs Rs Rs
It is in the form of The bit X changes in accordance with the instruction, and Rd indicates the destination register, and Rs indicates the source register. Generally, Rd is rewritten in principle in the operation of Rd <-Rd op Rs (except for C and CB instructions). The distinctive feature is the skip condition represented by S. When the operation result satisfies the skip condition, the next instruction is skipped. In L-16A, there is no general conditional branch instruction, so can we say that there is a +1 relative conditional jump attached to the operation instruction? Of course, to perform ordinary conditional branching, specify the B instruction as the instruction to skip. Of course, any instruction can be written, so if you want to call a subroutine depending on the condition, you will place an instruction such as AIR0, 1 etc. if you want to increment another register according to the condition.
There are 16 types of skip conditions as shown in the following table. In assembly language, operation instructions specify a skip condition at the end like OP Rd, Rs, Skip, etc. However, it can be omitted like OP Rd, Rs, in which case 0000 means no skip. You
SSSS	symbol	meaning
0 0 0 0		Without skipping
0 0 0 1	SKP	Unconditional skip
0 0 1 0	M	Negative result
0 0 1 1	PZ	Result is positive or zero
0 1 0 0	Z or E	Result is zero
0 1 0 1	NZ or NE	The result is not zero
0 1 1 0	MZ	Result is negative or zero
0 1 1 1	P	The result is positive
1 0 0 0	EZ	E register is zero
1 0 0 1	ENZ	E register is not zero
1 0 1 0	OZ	OVF is zero
1 0 1 1	ONZ	OVF is not zero
1 1 0 0	LMZ	Results are equal or small
1 1 0 1	LP	The result is great
1 1 1 0	LPZ	The result is great or equal
1 1 1 1	LM	The result is small

A, S, AND, OR, EOR instruction
Let's get into each argument of binary operation instruction. First, put together typical additions and subtractions and logical operations.
A 0 1 0 1 1 Rd Rd Rd SSS S 1 Rs Rs Rs
S 0 1 0 1 1 Rd Rd Rd SSS S 0 Rs Rs Rs
AND 0 1 1 0 1 Rd Rd Rd SSS S 1 Rs Rs Rs
OR 0 1 1 0 0 Rd Rd Rd SSS S 1 Rs Rs Rs
EOR 0 1 1 0 0 Rd Rd Rd SSS S 0 Rs Rs Rs
The A and S instructions for addition and subtraction set E and OVF correctly, and all skip conditions can be used. Since E and OVF do not change except for A and S among binary operation instructions, the result of the previous A or S instruction is saved, so skip conditions using AND R0, R1, EZ, etc. If specified, skip occurs depending on the result of the A, S instruction executed before that. Also, note that the carry condition does not change except for the A and S instructions, so the skip condition regarding the magnitude judgment has no meaning. You may want to use the bit manipulation instructions described below to determine if a particular bit of a register is set. As with EOR R0 and R0, if you specify the same register for Rd and Rs with EOR, the contents of that register can be 0. The LKit-16 assembler defines the instruction CLR Rn and automatically outputs the EOR Rn, Rn bit pattern.
Comparison instruction
C 0 1 0 1 0 Rd Rd Rd SSSS 1 Rs Rs Rs
CB 0 1 0 1 0 Rd Rd Rd SSSS 0 Rs Rs Rs
These two instructions perform skip judgment based on the result of performing Rd-Rs. There is no change in Rd, Rs, E, or OVF. However, large / small judgment and zero judgment work correctly. C compares the contents of all 16 bits of the register, and CB compares only the lower 8 bits of the register.
Movement command
MV 0 1 1 1 1 Rd Rd Rd SSSS 1 Rs Rs Rs
MVB 0 1 1 1 1 Rd Rd Rd SSSS 0 Rs Rs Rs
This command transfers the contents of Rs to Rd. The MV instruction transfers all the register contents, and the MVB instruction transfers only the lower 8 bits of the register. Skip judgment is performed according to the result. Specifying the same register for Rd and Rs does not change the contents of the register, so MVR0 and R0 have the same meaning as the NOP instruction. Also, for example, to determine whether the E register is 0 or 1, it may be written as MV R0, R 0, EZ, etc. To determine whether the content of the lower byte of a specific register is 0, MVB Rn, Rn , Z can be written. Although it is possible to use a bit manipulation instruction for STR to determine the contents of E and OVF, since the MV instruction is easier to specify the intention of E and OVF determination as the skip condition, the macro instruction can not be used. It may be easy to understand.
Swap instruction
BSWP 0 1 1 1 0 Rd Rd Rd SSSS 1 Rs Rs Rs
DSWP 0 1 1 1 0 Rd Rd Rd SSSS 0 Rs Rs Rs
These instructions are a kind of MV instruction that transfer the contents of Rs to Rd, but it is characterized by replacing some bit positions at that time. The BSWP instruction transfers the low byte of Rs to the high byte of Rd and the high byte of Rs to the low byte of Rd. The DSWP instruction moves bit 0 to bit 3 and bit 12 to bit 15 of Rs as it is to Rd, but bit 4 to bit 7 of Rs goes from bit 8 to bit 11 of Rd and bit 8 to bit of Rs 11 is transferred from bit 4 to bit 7 of Rd. In other words, if you divide 16 bit data into 1st digit to 4th digit, it is an instruction to exchange 2nd digit and 3rd digit and transfer. In L-16A, data transfer between memory and register is performed by L instruction and ST instruction, but it is always performed by 16 bits. Memory addresses are allocated in 16-bit words, not byte address machines. Therefore, when performing data processing in units of 1 byte, it will be carried out in combination with the MVB instruction etc while exchanging the upper byte and the lower byte by the BSWP instruction.
Decimal correction instruction
LAD 0 1 1 0 1 Rd Rd Rd SSSS 0 Rs Rs Rs
The LAD instruction is a slightly different instruction that tries Rd + Rs and loads 6 for the digit where the carry occurred, 0 for the digit that does not occur. When performing BCD operation, it is for performing decimal correction in combination with the A and S instructions. Because it is necessary to represent the carry of each digit by a flag for 16 bit operation, three auxiliary carry is required. Is it difficult to realize a correction instruction using a half carry like an 8 bit CPU? For example, when adding BCD with R0 and R1,
L R2, C6
A R2, R0; There is no carry here because R0 contains the BCD value
LAD R2, R1; Here, a correction value is set to R2.
A R0, R2
A R0, R1
;
C6: DC X'6666 '; 6666 in hexadecimal, a constant for correction
And so on. Subtraction is a little easier because no correction constant is required. Think of it as a puzzle. If it is necessary to carry out correction for a particular digit at 6 as in the case of the same BCD calculation as in the case of a clock, this can be achieved by changing the correction constant and adding a little code.
#### Shift instruction
There are two types of shift instructions: an SL instruction that shifts left and an SR instruction that shifts right. Each bit pattern is like this.
SL 0 0 1 0 0 RR R SSS S 1 1 E E
SR 0 0 1 0 0 RR R SSS S 1 0 E E
The RRR part is a register specification and the SSSS skip condition is the same as a binary operation instruction. Specifically, it is EE's E-register operation specification of EE, and it operates E-register as shown in the following table and then rotates by inserting E-register between bit 0 and bit 15 of the specified register. That is, in the case of an SL instruction, the contents of E register enter bit 15 of the designated register and the contents of bit 0 of the designated register enter E.
EE	symbol	Operation
0 0		No E register operation
0 1	RE	0-> E
Ten	SE	1-> E
1 1	CE	not (E)-> E

Although it is said to be a shift instruction but it is actually rotated, it will be a simple shift instruction that stuffs 0 if it is RE specified. Arithmetic shift right is performed if SRR n, RE or SRR n, SE is performed after judging whether the register contents are positive or negative.
#### Bit manipulation instruction and constant addition / subtraction instruction
Bit manipulation instructions and constant addition / subtraction instructions have the same instruction pattern in that they handle 4-bit constants. Let's arrange all the instruction patterns.
SBIT 0 0 1 1 1 RR R SSS S NNNN
RBIT 0 0 1 1 0 RR R SSS S NNNN
TBIT 0 0 1 0 1 RR R SSS S NNNN
AI 0 1 0 0 1 RR R SSS S NNN N
SI 0 1 0 0 0 RR R SSS S NNN N
The SBIT instruction sets the NNNNth bit of the register specified by RRR and then performs the skip determination. RBIT is a reset of a designated bit and TBIT is a test of a designated bit. For example, it can be judged by TBIT R0, 3, Z whether bit 3 of R0 is 1 or 0. AI adds a constant from 0 to 15 to the specified register. SI similarly subtracts a constant from 0 to 15.
#### I / O and MVI instructions
The RD, WT, and MVI instructions are similar in that they use 8-bit constants.
RD 0 0 0 1 1 RR R NNN N NNN N
WT 0 0 0 1 0 RR R NNN N NNN N
MVI 0 0 0 0 1 RR R NNN N NNNN
The RD instruction reads a value from the input device located at the I / O address specified by NNNNNNNN and stores it in the register. Conversely, the WT instruction writes the contents of the register to the specified I / O address. The MVI instruction loads the 8-bit constant specified by NNNNNNNN into the lower 8 bits of the specified register. The upper 8 bits do not change.
#### Other
Besides the above mentioned instructions, there are LPSW, H, PUSH, POP and RET instructions.
LPSW 0 0 1 0 0 0 0 0 0 0 0 0 0 1 LL
H 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0
PUSH 0 0 1 0 0 RR R 0 0 0 0 0 0 0 1
POP 0 0 1 0 0 RR R 0 0 0 0 0 0 1 0
RET 0 0 1 0 0 0 0 0 0 0 0 0 0 0 1 1
The LPSW instruction is an interrupt return instruction. LL indicates the interrupt level, and three types of 00, 01 and 10 can be specified. However, even if 11 is specified, the corresponding interrupt level does not exist but it operates and loads the contents of address 0006-0007 into STR and IC. The H instruction causes the processor to transition to the stop state. The CPU in the stopped state transitions to the operating state only by the STRT * signal. PUSH and POP are instructions to save and restore registers on the stack. The RET instruction is used to return from the subroutine called by the BAL instruction. Note that undefined instructions are interpreted as H instructions.
### Hardware details
Now let's change the mood and look at the hardware aspect.
First of all, the meaning of the usual pin arrangement and signal.
VBG 1 40 WRT
BS15 2 39 ADSD
BS14 3 38 ISYC *
BS13 4 37 ADAK *
BS12 5 36 BSRQ *
VSS 6 35 BSAV
BS11 7 34 CP2
BS10 8 33 CP1
BS09 9 32 DTAK *
BS08 10 31 DTSD
BS07 11 30 FSYC *
BS06 12 29 IOP
BS05 13 28 RST *
BS04 14 27 HALT *
BS03 15 26 CSRQ *
BS02 16 25 IRQ2 *
BS01 17 24 IRQ1 *
BS00 18 23 IRQ0 *
VDD 19 22 MANU *
VGG 20 21 STRT *
There are three power supplies: VBG, VDD and VGG. Assuming that VGG is +12 V and VDD is +5 V, VBG has a slightly odd value of -3 V. However, since VBG is a bias voltage and almost no current flows, it can be created by dividing a common negative voltage supply of -5 V or -12 V with a resistor.
BS15-BS00 will be the bus signal. Addresses and data are input / output in time division. However, BS00 is MSB (most significant bit) and BS15 is LSB (least significant bit). Be careful with this, as it is the opposite of assigning bit numbers to Intel, Motorola and DEC. This is also the same as the bit numbers of bit manipulation instructions. Including mini-computers in Japan, there have been a number of microprocessors even with computers whose bit 0 is MSB, like the TMS9900 series. This is a promise. In the sense that the weight is as small as the right digit, such as 1's digit, 2's digit, 4's digit, it may make sense to set the LSB to bit 0, and when drawing binary numbers, numbers will be ordered sequentially from the left It would be natural to say that. The point is, as long as it is unified in the manuals.
CP1 and CP2 require a 12 V swing as the 8080A clock signal. If IOP is 1, it is an I / O bus cycle; if it is 0, it is a memory bus cycle. If WRT is 1, writing is done from CPU, if 0, it is reading. RST * is a reset signal, and IRQ0 *, IRQ1 *, and IRQ2 * indicate interrupt request signals, and HALT * indicates whether the CPU is operating or not. This area is good for any CPU.
The signals that represent the bus cycle are BSRQ *, BSAV, ADSD, ADAK *, DTSD, and DTAK *. These six signals are actually two pairs of two, but with this bus and handshaking are performed to transfer data. First, when the CPU tries to start a bus cycle, it outputs BSRQ * to assert a bus use request. When the BSAV signal is returned from the bus controller and the bus use permission is issued, the ADSD is output and the address is output to BS15-BS00. The signal that all devices on the bus side have received an address is ADAK *, and when the CPU confirms this, it finally outputs DTSD. Reading data is just that, but writing data also outputs data to BS15-BS00 at the same time as DTSD. When the device addressed earlier receives DTSD, it outputs DTAK * after enough time for reading and writing. When the CPU receives DTAK *, one bus cycle is complete. Because it always waits for an acknowledge signal, it is an asynchronous bus. Note that the MN1640 of the family LSI includes a circuit that detects that the DTAK * signal does not return within a certain period of time, and sends a temporary DTAK * to the CPU and generates a bus blocking interrupt at the same time .
Since handshake is performed three times in one bus cycle, bus cycles that are as fast as possible can not be performed. Conversely, if you drive the bus with a strong buffer like SCSI, you can take the bus cycle for an arbitrary amount of time, so the total bus extension can be extended by about 10 m for reliable data transfer. . Around 1970, magnetic tape drives and disk subsystems were as large as refrigerators, so a short bus could not connect high-speed peripherals. It is the bus cycle of the mini-computer era that really pulled such an age. Even though it is high-speed, it has a transfer speed of at most 1.5 MByte / s (but it does not go as much as 1 Mcycle / s in terms of the transfer cycle in words). The mechanism to transfer addresses and data by time division also helps to reduce the number of wires and cost if the bus cable gets longer. Not only can the cost of wires and connectors be reduced, but the number of expensive high-performance bus buffers that drive wires can be reduced compared to transmitting addresses and data separately. If you think so, it looks like a reasonable mechanism. It is also suitable for multi-bus masters and tightly coupled multiprocessor systems to always issue bus use requests in BSRQ * before the bus cycle starts. On the other hand, it is an overarching mechanism for application to a small embedded system where the entire system is mounted on one printed circuit board and there is no bus master other than the CPU.
STRT * and MANU * are signals that specify the start mode (a little inaccurate). FSYC indicates an instruction fetch cycle, and ISYC * indicates an interrupt cycle.
The last remaining CSRQ * is a signal for the mini computer use. This is an abbreviation of ConSole ReQuest, and is valid only when the CPU is stopped. When the CPU detects that the signal has transitioned from high to low while this signal is valid, the CPU reads one word from address 0 in the I / O space and executes it as an instruction. It may be difficult to understand why this is a minicomputer signal. When the memory of the minicomputer was too small and debugging could not be done by making the debugger etc. resident in memory, machine language was executed one instruction at a time, and each time the contents of memory and registers were checked and debugged . You do this by manipulating the many switches and lights that line the console panel. When computers were built with transistors and simple ICs, it was better to extend the wires from the IC or device holding the value and connect it to the lamp on the console panel to check the contents of the register. However, once integrated into LSI, it is impossible to pull the wire from the register inside the LSI. Therefore, if a bit pattern equivalent to an instruction such as WT R0, 1 is inserted into I / O space address 0 and a CSRQ * pulse is given to the CPU, this CPU writes the contents of R0 to address 1 of the I / O port. . If you connect with the LED there, the contents of R0 will be displayed in one shot. Prepare a switch for register display on the console panel so that I / O port address 0 to WT R0, 1 or WT R1, 1 or WT X1, 1 can be read into the CPU accordingly. If you do, you can display the contents of all the registers on the console as needed. Conversely, if the contents of a specific switch group on the console panel are read when the CPU reads address 1 of the I / O port, such as RDR0, 1 or RDR2, 1 together with the CSRQ * signal The instruction can be read and any value can be set to the register. Also, if a B instruction (branch instruction) is read, the program can be executed from a specific address when the CPU becomes active next time. It can be said that it is unique for a microcomputer to be able to execute such a thing as hardware without using a monitor program even for 1 bit. The purpose is to include a function to realize a minicomputer-like console panel.
Actually, the same thing is realized with MITS Altair 8800b using Intel 8080, but it uses much more complicated circuits and ROM than do with L-16A. In a sense, Altair 8800b arranges the monitor program in a space that can not be seen from the user's memory space, so it does a lot of trouble, but most microcomputers do not require unnecessary application such as console panel It can be said that the L-16A incorporates a useless circuit, considering that it is used for Anyway, it's interesting hardware.
#### Interrupt mechanism
There are three levels of L-16A interrupts as described above. When the interrupt signal is accepted, the CPU saves the contents of IC and STR and reads the data of IC and STR for the interrupt routine. Since the IC-STR pair is called a program status word (PSW), it can be reworded as saving Old PSW (OPSW) and reading New PSW (NPSW). The L-16A stores the OPSW at a specific address in memory, not on the stack. In addition, NPSW is not determined by vector reading, but is read from a specific address in memory according to the interrupt level. Only the OPSW area and the NPSW area can be said to be addresses that have a special meaning for the CPU in the 64 KWord memory space (although 0 page can also be said to have a special meaning in addressing).
The OPSW area starts at address 0.
0000 Level 0 for STR backup
0001 Level 0 IC evacuation
0002 For level 1 STR evacuation
0003 For level 1 IC evacuation
0004 For level 2 STR evacuation
0005 For level 2 IC evacuation
The NPSW area is at the top of the first page after page 0 ends. The address is in hexadecimal notation.
0100 Level 0 STR information
0101 Level 0 IC Information
0102 Level 1 STR information
0103 Level 1 IC Information
0104 Level 2 STR Information
0105 Level 2 IC Information
Level 0 NPSW information is also referred to at auto start. If an interrupt service routine address is prepared in the IC portion of this NPSW area and an appropriate interrupt mask is applied to the STR portion, the interrupt service routine is called so that abnormal multiple interrupts are not generated by the interrupt signal. Will be Because it is not a stack structure, multiple interrupts of the same level can not be realized as it is. If multiple interrupts at the same level are required, it is necessary to save the PSW information recorded in the OPSW area to a stack-like data structure at the beginning of the interrupt service routine and then set the interrupt mask to the enabled state. Of course, in this case, the PSW information saved before the LPSW instruction is restored.
Since only PSW is automatically saved by an interrupt, other general-purpose registers must be saved if necessary in the interrupt service routine.
Since there are three interrupt request signals, practically, the outputs of multiple interrupt signal sources are wired-OR'd to accept interrupts. Note that by reading individual interrupt request information from the interrupt status register using the MN1640 RSC function, it is possible to check which of the 16 or less types of interrupt signal sources for each level actually made an interrupt request. .
Return to IC Collection